## Slide 1: Head-UP Display auto-alignment system
The cost of an airplane may be reduced in the future!
WHAT IS AN INERTIAL MEASUREMENT UNIT (IMU)?
An IMU contains a set of sensors that typically include an accelerometer, gyroscopes and/or magnetometer (compass). In this project, we used an IMU of model MPU-9250 from Sparkfun Electronics. An MPU-9250 IMU is as tiny as a quarter, yet it contains all three of the sensors mentioned above. A diverse set of sensors increases the degrees of freedom which improves data accuracy. In addition, in order to retrieve sensor data, we also used a microcontroller of model Metro-Mini 328 from Adafruit Industry to communicate with the IMU.
WHAT IS A HEAD-UP DISPLAY (HUD)?
A transparent display that is installed in a number of aircraft today. Located in the pilot’s forward field of view, a HUD presents flight information by using graphical, numerical and symbolical data. This device eliminates the need for pilots to continually transition from head-down instruments to head-up, out-the-window view during critical phases of flight.
Meet the Engineers
Group Members - Group #65
Krisna Irawan - irawank@oregonstate.edu
Jiongcheng Luo – luojio@oregonstate.edu
Drew Hamm – hammd@oregonstate.edu
Sponsors – Rockwell Collins, Inc.
Brandon Wilson
Weston Lahr
Flowchart
PROJECT OVERVIEW
Our project serves as a proof of concept for a new alignment methodology. This project is separated into three parts.
The configuration of hardware and communication between devices.
The development of an program that can find the HUD’s alignment offset in relation to the aircraft.
The design and implementation of a demonstration interface that visually presents the alignment results.
CURRENT HUD ALIGNMENT SYSTEM
Currently, a HUD obtains data from an aircraft’s Inertial Measurement Unit (IMU). To display precise and accurate information, the HUD must be carefully aligned to the IRU during installation. However, the current HUD installation process requires specialized equipment and epoxy which is time consuming, costly, and interrupts production line progress for the manufacturer.
HOW DID WE SOLVE THE PROBLEM?
Our demonstration system made use of two separate IMUs to generate the data that represents the individual points of origin for both the HUD and aircraft. Along with the IMUs, we used a microcontroller to process data and a PC to display the results.
CALIBRATION PROCESS & RESULT
Our project required a two part calibration process. First, each IMU was configured to output its individual sensor data. During IMU configuration, an initial calibration was performed to discover each sensors individual bias. Once the biases were known, we removed them from future readings. Next, the alignment offset discovery required a calibration process to produce a result within an acceptable range. We found the offset between two IMUs (airplane and HUD) after taking a number of samples from each device, the difference between each pair of samples and the average of those differences. Multiple data readings were required in each part of calibration to remove inaccuracies.
IMU - Sparkfun MPU-9250
Head-Up Display during flight
Pilot’s forward field of view
Microcontroller – Metro-Mini 328
Microcontroller wired to two IMUs
HYPOTHETICAL OUTCOME
Although we were not able to test the system using a real HUD on an aircraft, our project demonstrates how an inexpensive IMU can be used to accurately find an offset in alignment. This new alignment methodology points to a departure from the current HUD installation process by utilizing HUD mounted IMUs. Overall, this system proves that there is an opportunity to substantially cut HUD installation costs in the future.
NEW ALIGNMENT METHODOLOGY
The goal of this project is to improve the current HUD alignment systems by reducing the installation cost and time required to precisely align flight information to the HUD. Our client, Rockwell Collins, seeks a new alignment methodology that utilizes HUD mounted inertial measurement units.
By using a communication protocol we were able to access each IMU from the microcontroller. We used the Arduino development environment to program the microcontroller as well to debug data output. Data then was retrieved from each sensor and used to determine the alignment offset through statistical analysis. The results were then sent to the PC to be displayed.
Data flow between hardware components
Reading IMU data in Arduino Development Environment
Notes: If tri-fold mounting at SMS – make sure no text or image is in-between the two vertical guide lines; this space will be cut away. To view the vertical guide lines: Select “View” from the main menu, select “Guides” from the pull down menu, and lastly select “Static Guides”.